## Slide 1: Implicit-Storing and Redundant-Encoding-of-Attribute Information in Error-Correction-Codes
Yiannakis Sazeides1, Emre Ozer2, Danny Kershaw3, Panagiota Nikolaou1,
Marios Kleanthous1, Jaume Abella4
1University of Cyprus, 2ARM, 3NXP, 4Barcelona Supercomputing Center
HARPA
MICRO 46, Davis, California, December 9th 2013

## Slide 2: Logical and Physical Memory Organization
Logical Organization (programming model): a table with addresses and data
Physical Organization (manufacturing, cost, performance ):
  multi level hierarchy of arrays (DRAM, cache etc)
  an array consist of multiple blocks each with a unique address
  each block with many words
Address
Data
Address
Data
word
block
Logical Organization
Physical Organization

## Slide 3: Reliability Implications on the Memory Organization
  Protect data from faults
  add ECC code to detect and correct errors [Hamming 1950]
  Increase availability
    add Poison bit to minimize failures from uncorrectable errors [Weaver 2004]
Address
…

## Slide 4: Security Implications on the Memory Organization
  Prevent malicious attacks
    Track dynamically dependence to input data with taint bits [Suh 2004]
Address
…

## Slide 5: Performance and Energy Implications on the Memory Organization
  Performance and energy benefits
    Track the dirty status of sub-block with extra bits [Wang 2009]
    Full-Empty bits [Smith 1981]
    Tagged Memory [Gumpertz 1983]
    …
Address
…

## Slide 6: What we need!
Extra information in memory arrays for reliability, availability, security, performance, energy, …
  But:
    more area overheads
    slower memory
    consumes more energy
Address
…

## Slide 7: What we propose!!
1. Implicit storing (IS)
  Do not store the extra information in the array
  Encode the extra information in the ECC codes
   Cost-effective, minimal impact on:
    Area
    Energy
    Performance
   Weakens strength of ECC for data
2. Redundant Encoding of Attribute Information (REA)
  Encode the same information in multiple codewords of a block
   Recovers some ECC code strength lost due to IS
Address
…
ECC
ECC
Data
Data

## Slide 8: Outline
Background
Implicit Storing (IS)
Redundant- Encoding-of-Attributes (REA)
IS with REA
Conclusions

## Slide 9: Terminology
Faults: incorrect state of hardware or software resulting from physical defect, design flaw, or operator error
  Faults introduced during system design
  Faults introduced during manufacturing
  Faults that occur during operation
Error: an incorrect state resulting from an active fault,
  e.g an incorrect value in memory
Failure: system level effect of an error (user-visible)
  e.g system produces incorrect result of computation
Error
Fault

## Slide 10: Protecting data from errors
m
generate
m
k
m
Data
ECC
Write
How it works:
  Write:
  Generate ECC bits(k) from data bits (m)
  Store data and ECC bits in the array

## Slide 11: Protecting data from errors
How it works:
  Read:
  Read data bits (m) and ECC bits (k) from the array
  Perform error checking
  The decoder produce a
  syndrome that indicates:
    No error
    Error:
      Correctable
      Uncorrectable
ECC(m)
m | k
m
k
Data
ECC
Read
decoder
Error
No error
Unrecoverable
Correct
Compare

## Slide 12: Error detection codes
Parity bit
  Includes d-data bits and 1-extra bit
  Even/odd parity code - the extra bit is set so that the total number of 1's in the (d+1)-bit word (including the parity bit) is even/odd
  P4=1 ^ 2 ^ 3
1 | 2 | 3
Data
Parity
4
d
1 | 2 | 3
0 | 1 | 0
Data
Parity
4
1 | 2 | 3
0 | 1 | 0
4
1
Data
Parity’
1 | 2 | 3
0 | 1 | 0
4
1
Compare
Syndrome:1^1=0
Write
Read

## Slide 13: Parity bit in the presence of data error
  P4=1 ^ 2 ^ 3
1 | 2 | 3
0 | 1 | 0
Data
Parity
4
1 | 2 | 3
0 | 1 | 0
4
1
1 | 2 | 3
1 | 1 | 0
4
1
Data
Parity’
1 | 2 | 3
1 | 1 | 0
4
0
Compare
Syndrome:1^0=1
Write
Read

## Slide 14: Error correction codes
ECC codes
Detection and Correction capability
  Single Error Correction Double Error Detection (SECDED)
  A data word with d bits is encoded into an ECC code with k bits d < 2k-1 – k
Parity matrix that produce the ECC check bits [Hsiao 1970]:
              P4=1 ^ 2
              P5=1 ^ 3
              P6= 2 ^ 3
              P7=1 ^ 2 ^3
1 | 2 | 3
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 |  |  |  | 
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 5 | 6 | 7
 | 1 | 2 | 3
4 | 1 | 1 | 0
5 | 1 | 0 | 1
6 | 0 | 1 | 1
7 | 1 | 1 | 1
d
k

## Slide 15: ECC codes in the presence of data error
Parity matrix that produce the ECC check bits [Hsiao 1970]:
              P4=1 ^ 2
              P5=1 ^ 3
              P6= 2 ^ 3
              P7=1 ^ 2 ^3
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1 | 2 | 3
4 | 1 | 1 | 0
5 | 1 | 0 | 1
6 | 0 | 1 | 1
7 | 1 | 1 | 1
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 0 | 1 | 0 | 1 | 1
Data
ECC’
Compare
Syndrome:
0^1=1 0^0=0
    0^1=1
    0^1=1
Write
Read
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 0 | 1 | 1

## Slide 16: ECC codes in the presence of two data error
Parity matrix that produce the ECC check bits [Hsiao 1970]:
              P4=1 ^ 2
              P5=1 ^ 3
              P6= 2 ^ 3
              P7=1 ^ 2 ^3
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1 | 2 | 3
4 | 1 | 1 | 0
5 | 1 | 0 | 1
6 | 0 | 1 | 1
7 | 1 | 1 | 1
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 1 | 1 | 1 | 0 | 0
Data
ECC’
Compare
Syndrome:
0^1=1 0^1=1
    0^0=0
    0^0=0
Write
Read

## Slide 17: Shortened codes
  The number of protected bits is smaller than the maximum number that can be protected
  e.g. SECDED code
    single error correction, double error detection
    k check bits can provide protection for d bits as long as:
    d < 2k-1 – k
    for k=8 bits  maximum d=120 bits
    If protected data is 64 bits  code can protect 56 extra bits

## Slide 18: Outline
Background
Implicit Storing (IS)
Redundant- Encoding-of-Attributes (REA)
IS with REA
Conclusions

## Slide 19: Implicit-Storing (IS)
Basic Idea:
  Extend the logical capacity of a memory array without increasing its physical capacity
How:
    Do not save the extra information but encode it in the ECC
    On writes, extra information is erased using erasure coding
      Erasure: a specific bit position of the data with an unknown value
    On reads, the extra information is produced using erasure recovery
0 | 0 | ? | 0
Data
0 | 0 | 1 | 0
Data
…
Address
…
ECC
ECC
Data
Data

## Slide 20: Example parameters
On a write
Assume 3 bit data (1,2,3)
Protected with 4 bit SECDED code (4,5,6,7)
  Maximum number of protected bits is 4 (shortened code)
    p < 2k-1 – k
    Extra space for Implicit store  1 bit (IS)
Parity matrix that produce the ECC check bits [Hsiao 1970]:
              P4=1 ^ 2 ^ IS
              P5=1 ^ 3 ^ IS
              P6= 2 ^ 3 ^ IS
              P7=1 ^ 2 ^ 3
On a read
A syndrome is produced:
  Syndrome=Stored ECC ^ Produced ECC
  Indicates the type of the error
  Syndrome decoding based on the above parity matrix:
    Zero Syndrome: No error
    Odd Syndrome: Odd errors >1  Single error correction
    Even Syndrome: Even errors >2 Uncorrectable
1 | 2 | 3
Data
ECC
IS
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 |  |  |  | 
Data
ECC
1
IS
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 |  |  | 
1
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 |  | 
1
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 
1
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
1
4 | 5 | 6 | 7
 | 1 | 2 | 3
4 | 1 | 1 | 0
5 | 1 | 0 | 1
6 | 0 | 1 | 1
7 | 1 | 1 | 1

## Slide 21: Example of 1 bit Implicit Storing (IS)
On a write:
  Data and IS are encoded in the ECC code
  Then IS erased
On a read:
  Produce the implicit bit with two decodings instead of one
  One assumes IS=0 and the other assumes IS=1
  Infer implicit bit from codeword with fewer errors
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
…
1 | 2 | 3
0 | 0 | 0
Data
ECC
1
IS
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Data
ECC
…
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3
0 | 0 | 0
Data
…
?
IS
0
IS
1
IS
1
IS
Read
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
SYNDROME
1110
SYNDROME
0000
Write
Single error
No error
4 | 5 | 6 | 7
0 | 0 | 0 | 0
IS infers correctly the IS bit

## Slide 22: Example of IS in the presence of data error
…
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 1 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 1 | 1 | 1 | 1 | 0
Data
ECC
…
?
IS
0
IS
1
IS
Read
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 1 | 1 | 1 | 1 | 0
Data
ECC
Syndrome
1001
Syndrome
0111
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
…
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
Data
ECC
1
IS
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Data
ECC
…
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Write
1 | 2 | 3
0 | 0 | 0
Data
1
IS
Double error
Single error
IS correct the error and infers correctly the IS bit

## Slide 23: Corner Case with 2 data errors
Decoder chose the syndrome that indicates fewer errors Produce incorrect legal codeword
Data are faulty and the IS is not the right 
…
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 1 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 1 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3
1 | 1 | 1
Data
…
?
IS
0
IS
1
IS
0
IS
Read
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 1 | 1 | 1 | 1 | 0
Data
ECC
Syndrome
0010
Syndrome
1100
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
…
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0
Data
ECC
1
IS
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Data
ECC
…
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 1 | 1 | 1 | 0
Write
Single error
Double error
Without IS uncorrectable
With IS miscorrected data
Can we minimize this error code strength reduction?

## Slide 24: Outline
Background
Implicit Storing (IS)
Redundant- Encoding-of-Attributes (REA)
IS with REA
Conclusions

## Slide 25: Redundant Encoding of Attributes (REA)
The granularity for ECC protection is often smaller than the granularity of block transfer
    e.g. ECC code protects 64 bit data, and the block size is 512 bits
On writes encode the same information in multiple codewords of a block
  Correlated words: encode same attribute information
On reads when there is an error decode the correlated codewords to detect and correct the error
Address
…
ECC
ECC
Data
Data

## Slide 26: IS + REA=IREA
How it works:
  When one syndrome has no error: business as usual
  Otherwise with errors in both syndromes
    Read multiple correlated locations and produce their codewords
    The decoder uses many codewords to determine data and implicit bit
Changes:
  Extend generate and check units to consider attributes
  In case of an error need to read and generate syndromes of correlated locations
  Need new decoder that uses correlated location codes as inputs to decide reaction

## Slide 27: IREA: Example of a word with 2 data errors
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 1 | 1 | 1 | 1 | 0
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 1 | 1 | 1 | 1 | 0
Data
ECC
…
?
IS
0
IS
1
IS
Read Word 1
1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 0 | 0 | 0 | 0 | 1 | 1
Data
ECC
1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 0 | 0 | 0 | 0 | 1 | 1
Data
ECC
1 | 2 | 3
1 | 0 | 0
Data
…
?
IS
0
IS
1
IS
1
IS
Syndrome
1110
Syndrome
0000
Read Word 2
Syndrome
0010
Syndrome
1100
Single error
Double error
Single error
No error
With IS miscorrected data 
With IREA uncorrectable 

## Slide 28: Some key design implications
No changes in the SRAM macros and DIMMs
Changes limited in the cache and memory controllers
Required changes are minimal, handful of gates

## Slide 29: What else discussed in the paper
How Implicit Storing and Redundant Encoding of Attributes reacts in the presence of errors in correlated words
Discuss Error Code Tagging (ECT) [Gumpertz 1983]
  ECT useful for encoding attributes that are available at write and read time
  Explain differences with IS
  How to combine ECT + REA=EREA
Temporal and Spatial reliability analysis for single bit transient errors
Discuss performance overheads of IREA and EREA
Discuss selective use of IS and REA
Area, Delay and Scalability analysis

## Slide 30: Summary and Conclusions (1)
Many techniques to improve performance, reliability, availability, security, energy rely on extra information stored in memory
Propose: Implicit Storing and Redundant Encoding of Attributes
Implicit Storing: extend the logical capacity of a memory array without increasing its physical capacity
Save extra information
  without area and energy overheads
  with minimal performance impact
IS causes reduction in the code strength

## Slide 31: Summary and Conclusions (2)
Redundant encoding of Attributes: redundantly encode the same attributes in multiple codewords
REA can minimize the reduction of the code strength
Applicable to both IS and ECT
Minimal impact on performance
Future work: Applications and detailed analysis of correlated errors

## Slide 32: Acknowledgments
“Eurocloud” and “Harpa” FP7 Projects
HIPEAC FP7 Network of Excellence
Spanish Ministry of Science and Innovation

## Slide 33
email: panagiota.nikolaou@cs.ucy.ac.cy
room: ΘΕΕ01 124
Thanks!